## Slide 2
PROJECT OVERVIEW
What is Cosmic Wars?
Cosmic Wars is an interactive, space-themed mechatronics game that combines physical engineering with real-time decision-making. Players answer trivia questions to unlock ball shooters, scoring points by hitting targets with color-sorted balls — all controlled by Arduino.
🎮 Interactive Gameplay
Joystick-controlled ball shooters for real-time play
🤖 Arduino-Powered
Dual microcontrollers handle sensing & actuation
🔵 Color Sorting
Automated sorting of green & white balls via sensor
🏆 Scoring System
Left target 100pts, centre & right 50pts each

## Slide 3
SYSTEM ARCHITECTURE
Block Diagram
Key Signals
Color signal
Sensor → Arduino
Input A / B
Buttons → Arduino
Open/Close
Arduino → Entry gate servo
Trigger
Arduino → Lifting motor
Question data
Arduino → LCD display
Unlock gates
Arduino → Sorting servos

## Slide 4
HARDWARE CONNECTIONS
Wiring Diagram
Power (12V/5V)
Ground (GND)
Signal / Data
Control Lines

## Slide 5
GAME LOGIC
System Flowchart
01
Ball Entry & Detection
2 balls enter the path. Color sensor reads ball at the detection gate.
02
Sorting by Color
Ball is lifted and routed to green or white path by Arduino servos.
03
Trivia Question
LCD displays question. Player presses Button A or B to answer.
04
Gate Unlock
Correct answer → servo gate opens, ball moves to shooter lane.
05
Player Shoots
Manual joystick control. Ball hits Left (100 pts) or other (50 pts).
06
Closed Loop Repeats
Ball returns to path, cycle restarts automatically.

## Slide 6
HARDWARE SPECIFICATIONS
Components & Parts
Microcontrollers
▸ 2× Arduino Uno
▸ Dual-board architecture
▸ Master + slave configuration
Sensors & Inputs
▸ Color sensor (green/white detection)
▸ 2× Joystick modules
▸ 4× Push buttons (A/B per player)
Actuators
▸ 5× Servo motors (gates & shooter)
▸ 2× DC motors
▸ Lifting mechanism motor
▸ Cooling fan
Power & Display
▸ 12V / 20A main supply
▸ 3× AAA battery pack (5V)
▸ 4× Voltage regulators
▸ LCD display screen

## Slide 7
GAMEPLAY
Scoring & Rules
LEFT TARGET
100
pts
Hardest to hit
CENTRE TARGET
50
pts
Medium difficulty
RIGHT TARGET
50
pts
Medium difficulty
Game Rules
🟢 Green balls go to the Green shooter lane
⚪ White balls go to the White shooter lane
❓ Answer the trivia question before your gate opens
🎮 Use the joystick to aim and shoot the ball
🔄 Balls automatically return to the path — closed loop
🏆 Highest score after all balls cycled wins the round

## Slide 8
🚀
COSMIC WARS
Thank You · Questions Welcome
Ain Shams University • Faculty of Engineering • Mechatronics Dept. • mct231